## Slide 1: Significance of Research
Is the current approach for accounting for dynamic amplification adequate?
Dynamic amplification of a structure is highly dependent on the specific profile in-situ.
Cannot be estimated without considering the bridge
Current methods likely to remain conservative at strength limit states (multiple simultaneous vehicles)

## Slide 2: Significance of Research
How can the dynamic amplification of an existing bridge be estimated?
Operational monitoring
Simulation with measured profile

## Slide 3: Significance of Research
What are better ways of accounting for VBI?
Dependent on application
3D FE modeling with “moving-mass” analysis
Simplified model is less accurate but conservative and easy to implement

## Slide 4: Significance of Research
What measures can be taken to ensure a bridge does not experience high dynamic amplification?
Increase bridge stiffness
Specify and maintain a smooth profile

## Slide 5: Significance of Research
What can be done if a bridge is exhibiting high dynamic amplification?
Likely due to profile; confirm.
If profile is the culprit how to mitigate
  Smooth profile – Rolling straightedge inadequate at common limits
  Reduce vehicle speed

## Slide 6: Significance of Research
Do platoons pose additional risk to bridge performance?
Higher amplification may occur when the bridge is subjected to repeated vehicle loading
For small headway spacing, static load effect is increased and dynamic amplification decreases
Use amplification factor as computed for single vehicle